Optical DMB Test Firmware

December 6, 2012

- Addresses

| Address | Access | Function |
| --- | --- | --- |
| Base + 0 | R/W | GTX Control Register, all links. Bit[0]: RXENMCOMMAALIGN_IN; Bit[1]: RXENPCOMMAALIGN_IN; Bits[8:7]: TXCHARISK_IN[1:0]; Bits[11:9]: LOOPBACK_IN[2:0]; Bits[15:13]: RX/TX_PLLREFSELDY_IN[2:0] |
| Base + 2 | R/W | GTX PRBS Control Register, all links, Bits[3:1]: RXENPRBSTST_IN[2:0] |
| Base + 4 | R | Bit[0] – LVMB_SDOUT; Bits[7:1]=0; Bits[15:8]=R_LVMB_PON[7:0] |
| Base + 6 | R | STATUSA(15:0) Bytes Aligned status from 12 GTX links |
| Base + 8 | R | STATUSB(15:0) Comma Detect status from 12 GTX links |
| Base + a | R | STATUSC(15:0) PLLKDET status from 12 GTX links |
| Base + c | R | STATUSD(15:0) RESETDONE status from 12 GTX links |
| Base + e | R | Firmware Date (bits[4:0] – day; bits[8:5] – month; bits[12:9] – year, bits[15:13]=0) |
| Base + 10 | W | Reset internal buffers and FIFOs (dataless) |
| Base + 12 | W | Send data from FIFO_A to GTXs (dataless) |
| Base + 14 | W | Reset COMMADET latches for all GTX links (dataless) |
| Base + 16 | W | Reset PRBS error counters, all GTX links (dataless) |
| Base + 18 | W | GTXTXRESET_IN, GTXRXRESET_IN; Reset all GTXs (dataless) |
| Base + 1a | W | PLLRXRESET_IN, PLLTXRESET_IN; Reset PLL TX/RX, all GTX links (dataless) |
| Base + 1c | W | TX/RX DLYALIGNRESET, all GTX links (dataless) |
| Base + 1e | R/W |  |
| Base + 20 | R | PRBS error counter, GTX link 1 |
| Base + 22 | R | PRBS error counter, GTX link 2 |
| Base + 24 | R | PRBS error counter, GTX link 3 |
| Base + 26 | R | PRBS error counter, GTX link 4 |
| Base + 28 | R | PRBS error counter, GTX link 5 |
| Base + 2a | R | PRBS error counter, GTX link 6 |
| Base + 2c | R | PRBS error counter, GTX link 7 |
| Base + 2e | R | PRBS error counter, GTX link 8 |
| Base + 30 | R | PRBS error counter, GTX link 9 |
| Base + 32 | R | PRBS error counter, GTX link 10 |
| Base + 34 | R | PRBS error counter, GTX link 11 |
| Base + 36 | R | PRBS error counter, GTX link 12 |
| Base + 38 | R | CMDREG[15:0] register from CCB. CLK=CMDSTR. Bits[5:0]=CMD[5:0], bits[15:6]=0 |
| Base + 3a | R | L1A counter, 16 bits |
| Base + 3c | R | BC0 counter, 16 bits |
| Base + 3e | R | DATREG[15:0] register from CCB. CLK=DATSTR. Bits[7:0]=DAT[7:0], bits[15:8]=0 |
| Base + 40 | R/W | FIFO_A1 (to GTX TX[15:0] link 1) |
| Base + 42 | R/W | FIFO_A2 (to GTX TX[15:0] link 2) |
| Base + 44 | R/W | FIFO_A3 (to GTX TX[15:0] link 3) |
| Base + 46 | R/W | FIFO_A4 (to GTX TX[15:0] link 4) |
| Base + 48 | R/W | FIFO_A5 (to GTX TX[15:0] link 5) |
| Base + 4a | R/W | FIFO_A6 (to GTX TX[15:0] link 6) |
| Base + 4c | R/W | FIFO_A7 (to GTX TX[15:0] link 7) |
| Base + 4e | R/W | FIFO_A8 (to GTX TX[15:0] link 8) |
| Base + 50 | R/W | FIFO_A9 (to GTX TX[15:0] link 9) |
| Base + 52 | R/W | FIFO_A10 (to GTX TX[15:0] link 10) |
| Base + 54 | R/W | FIFO_A11 (to GTX TX[15:0] link 11) |
| Base + 56 | R/W | FIFO_A12 (to GTX TX[15:0] link 12) |
| Base + 58 | R/W | FIFO_A13 (to TX1[15:0] transmitter) |
| Base + 5a | R/W | FIFO_A14 (to TX2[15:0] transmitter) |
| Base + 5c | R/W |  |
| Base + 5e | R/W |  |
| Base + 60 | R/W | FIFO_B1 (from RX[15:0] GTX link 1) |
| Base + 62 | R/W | FIFO_B2 (from RX[15:0] GTX link 2) |
| Base + 64 | R/W | FIFO_B3 (from RX[15:0] GTX link 3) |
| Base + 66 | R/W | FIFO_B4 (from RX[15:0] GTX link 4) |
| Base + 68 | R/W | FIFO_B5 (from RX[15:0] GTX link 5) |
| Base + 6a | R/W | FIFO_B6 (from RX[15:0] GTX link 6) |
| Base + 6c | R/W | FIFO_B7 (from RX[15:0] GTX link 7) |
| Base + 6e | R/W | FIFO_B8 (from RX[15:0] GTX link 8) |
| Base + 70 | R/W | FIFO_B9 (from RX[15:0] GTX link 9) |
| Base + 72 | R/W | FIFO_B10 (from RX[15:0] GTX link 10) |
| Base + 74 | R/W | FIFO_B11 (from RX[15:0] GTX link 11) |
| Base + 76 | R/W | FIFO_B12 (from RX[15:0] GTX link 12) |
| Base + 78 | R/W | FIFO_B13 (from RX[15:0] receiver RX1) |
| Base + 7a | R/W | Bit[0]=LVMB_SCLK; Bit[1]=LVMB_SDI; Bit[2]=LVMB_PONLOAD; Bit[3]=LVMB_PONOE, Bits[15:4] – N/D |
| Base + 7c | R/W | Bits[6:0]=LVMB_CSB[6:0]; Bit[7] – N/D; Bits[15:8]=LVMB_PON[7:0] |
| Base + 7e | R/W | Status register, Bit[0]=QPLLLOCKED; Bit[1]=QPLLERROR; Bit[2]=MMCM locked; Bits[11:3]=0; Bit[12]=RX2SD; Bit[13]=RX1SD; Bit[14]=TX2FAULT; Bit[15]=TX1FAULT |

- GTX links

| Bank | Link | Pin | ODMB assignment |
| --- | --- | --- | --- |
| 112 | MGTCLK0P | AK6 | GL1_CLK |
|  | MGTCLK0N | AK5 | - |
|  | MGTCLK1P | AH6 | - |
|  | MGTCLK1N | AH5 | - |
|  | MGTRXP0 | AP5 | GL1_RXP |
|  | MGTRXN0 | AP6 | GL1_RXN |
|  | MGTTXP0 | AP1 | GL1_TXP |
|  | MGTTXN0 | AP2 | GL1_TXN |
|  | MGTRXP1 | AM5 | - |
|  | MGTRXN1 | AM6 | - |
|  | MGTTXP1 | AN3 | - |
|  | MGTTXN1 | AN4 | - |
|  | MGTRXP2 | AL3 | - |
|  | MGTRXN2 | AL4 | - |
|  | MGTTXP2 | AM2 | - |
|  | MGTTXN2 | AM2 | - |
|  | MGTRXP3 | AJ3 | - |
|  | MGTRXN3 | AJ4 | - |
|  | MGTTXP3 | AK1 | - |
|  | MGTTXN3 | AK2 | - |
| 113 | MGTCLK0P | AD6 | GL0_CLK |
|  | MGTCLK0N | AD5 | - |
|  | MGTCLK1P | AB6 | TCLK_P |
|  | MGTCLK1N | AB5 | TCLK_N |
|  | MGTRXP0 | AG3 | GL0_RXP |
|  | MGTRXN0 | AG4 | GL0_RXN |
|  | MGTTXP0 | AH1 | GL0_TXP |
|  | MGTTXN0 | AH2 | GL0_TXN |
|  | MGTRXP1 | AF5 | - |
|  | MGTRXN1 | AF6 | - |
|  | MGTTXP1 | AF1 | - |
|  | MGTTXN1 | AF2 | - |
|  | MGTRXP2 | AE3 | GTX_0_P (from J3) |
|  | MGTRXN2 | AE4 | GTX_0_N (from J3) |
|  | MGTTXP2 | AD1 | GRX_0_P (from J3) |
|  | MGTTXN2 | AD2 | GRX_0_N (from J3) |
|  | MGTRXP3 | AC3 | - |
|  | MGTRXN3 | AC4 | - |
|  | MGTTXP3 | AB1 | - |
|  | MGTTXN3 | AB2 | - |
| 114 | MGTCLK0P | V6 | CLKCDC_P4 |
|  | MGTCLK0N | V5 | CLKCDC_N4 |
|  | MGTCLK1P | T6 | CLKCDC_P3 |
|  | MGTCLK1N | T5 | CLKCDC_N3 |
|  | MGTRXP0 | AA3 | ORX2_05P |
|  | MGTRXN0 | AA4 | ORX2_05N |
|  | MGTTXP0 | Y1 | - |
|  | MGTTXN0 | Y2 | - |
|  | MGTRXP1 | W3 | ORX2_01P |
|  | MGTRXN1 | W4 | ORX2_P1N |
|  | MGTTXP1 | V1 | - |
|  | MGTTXN1 | V2 | - |
|  | MGTRXP2 | U3 | ORX2_04P |
|  | MGTRXN2 | U4 | ORX2_04N |
|  | MGTTXP2 | T1 | - |
|  | MGTTXN2 | T2 | - |
|  | MGTRXP3 | R3 | ORX2_02P |
|  | MGTRXN3 | R4 | ORX2_02N |
|  | MGTTXP3 | P1 | - |
|  | MGTTXN3 | P2 | - |
| 115 | MGTCLK0P | P6 | CLKCDC_P2 |
|  | MGTCLK0N | P5 | CLKCDC_N2 |
|  | MGTCLK1P | M6 | CLKCDC_P6 |
|  | MGTCLK1N | M5 | CLKCDC_N6 |
|  | MGTRXP0 | N3 | ORX2_03P |
|  | MGTRXN0 | N4 | ORX2_03N |
|  | MGTTXP0 | M1 | - |
|  | MGTTXN0 | M2 | - |
|  | MGTRXP1 | L3 | ORX2_11P |
|  | MGTRXN1 | L4 | ORX2_11N |
|  | MGTTXP1 | K1 | - |
|  | MGTTXN1 | K2 | - |
|  | MGTRXP2 | K5 | ORX2_10P |
|  | MGTRXN2 | K6 | ORX2_10N |
|  | MGTTXP2 | H1 | - |
|  | MGTTXN2 | H2 | - |
|  | MGTRXP3 | J3 | ORX2_12P |
|  | MGTRXN3 | J4 | ORX2_12N |
|  | MGTTXP3 | F1 | - |
|  | MGTTXN3 | F2 | - |
| 116 | MGTCLK0P | H6 | CLKCDC_P7 |
|  | MGTCLK0N | H5 | CLKCDC_N7 |
|  | MGTCLK1P | F6 | CLKCDC_P5 |
|  | MGTCLK1N | F5 | CLKCDC_N5 |
|  | MGTRXP0 | G3 | ORX2_07P |
|  | MGTRXN0 | G4 | ORX2_07N |
|  | MGTTXP0 | D1 | - |
|  | MGTTXN0 | D2 | - |
|  | MGTRXP1 | E3 | ORX2_08P |
|  | MGTRXN1 | E4 | ORX2_08N |
|  | MGTTXP1 | C3 | - |
|  | MGTTXN1 | C4 | - |
|  | MGTRXP2 | D5 | ORX2_09P |
|  | MGTRXN2 | D6 | ORX2_09N |
|  | MGTTXP2 | B1 | - |
|  | MGTTXN2 | B2 | - |
|  | MGTRXP3 | B5 | ORX2_06P |
|  | MGTRXN3 | B6 | ORX2_06N |
|  | MGTTXP3 | A3 | - |
|  | MGTTXN3 | A4 | - |

- LEDs

LED1 (top right, red): CCB clock (~4Hz)

LED2 (top left, green): Start data transmission from FIFO_A on VME or CCB decoded command=30hex; with one-shot

LED3 (red, below LED1): VME DTACK produced by the FPGA, with one-sot

LED4 (green, under LED2): Geographical Address decoded

LED5 (red, under LED3): VME DTACK produced by the discrete logic interface (address xxFFFCh), with one-shot

LED6 (green, under LED4): QPLL locked

LED7 (red, under LED5): TXCLKOUT from the GTX (~4Hz)

LED8 (green, under LED6): MMCM locked

LED9 (red, under LED7): 160MHz clock from the GTX clock driver 0 (~4Hz)

LED10 (green, under LED8): off, not used

LED11 (red, under LED9): 160MHz clock from the GTX clock driver 1 (~4Hz)

LED12 (green, under LED10): off, not used

LED13 (yellow, bottom left):  DONE from the FPGA

LED14 (yellow, bottom right) INIT_B from the FPGA

- Test Points

TP65: 6 ns pulse upon write to (base+7e) address

TP63:  QPLL locked

TP67: 160Mhz clock from GTX clock driver 0

TP69: 160Mhz clock from GTX clock driver 1

- Example of C code to access the LVMB board

// init; ODMB in slot 17

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// set CS=0 for the selected ADC

// FFFE - ADC1 (U30); FFFD - ADC2 (U31); FFFB - ADC3 (U32); FFF7 - ADC4 (U33);

// FFEF - ADC5 (U34); FFDF - ADC6 (U35); FFBF - ADC7 (U36);

vme->Write((bt_devaddr_t)0x88007c, (WORD)0xFFFE);

// start bit

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x3);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// select a channel CH0-CH7 of the chosen ADC (channel 0 below)

// SEL2

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// SEL1

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// SEL0

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// select full scale 0-10V

// RNG=1

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x3);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// BIP=0

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// normal mode, external clock mode

// PD1=0

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// PD0=1

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x3);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x2);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// generate 4 external clocks

// clock 9

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// clock 10

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// clock 11

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// clock 12

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

// read MSB bit 11 on a falling edge of the 5th clock

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 11 = "  << Data1 <<  endl;

// read bit 10

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 10 = "  << Data1 <<  endl;

// read bit 9

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 9 = "  << Data1 <<  endl;

// read bit 8

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 8 = "  << Data1 <<  endl;

// read bit 7

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 7 = "  << Data1 <<  endl;

// read bit 6

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 6 = "  << Data1 <<  endl;

// read bit 5

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 5 = "  << Data1 <<  endl;

// read bit 4

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 4 = "  << Data1 <<  endl;

// read bit 3

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 3 = "  << Data1 <<  endl;

// read bit 2

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 2 = "  << Data1 <<  endl;

// read bit 1

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 1 = "  << Data1 <<  endl;

// read bit 0

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x1);

vme->Write((bt_devaddr_t)0x88007a, (WORD)0x0);

vme->Read((bt_devaddr_t)0x880004, (WORD*)&Data);

Data1=Data&0x0001;

cout << hex << " Bit 0 = "  << Data1 <<  endl;

// set CS=1

vme->Write((bt_devaddr_t)0x88007c, (WORD)0xFFFF);

// end reading the lvmb