Optohybrid Board BOM

27 July, 2018

| Part Numbers | Part | Package | Number per board | Comments |
| --- | --- | --- | --- | --- |
| U1 | Xilinx XC7A75T-2FGG484C | BGA484 | 1 | Top |
| U2, U3 | GBTx ASIC | BGA400 | 2 | Top |
| U4 | SCA ASIC | LFBGA196 | 1 | Top |
| U5, U9, U11, U23, U24, U28, U29, U36 | SN74AVC2T45DCTR | SM8 | 8 | Top or bottom |
| U6, U7, U8 | Micrel MIC69502WR | 7-pin S-PAK | 3 | Top |
| U10, U22 | VTRX | (pluggable into Tyco 1888247-1 connector) | 2 | Bottom |
| U12, U13, U14, U16, U17, U18, U19, U20, U21 | SN65LVDT2DBV | 5-pin SOT-23 | 9 | Top or bottom |
| U15 | SN74CBTLV3861PWR | TSSOP24 | 1 | Top or bottom |
| U32, U37 | SN74AUP1G04DBVR | 5-pin SOT-23 | 2 | Top or bottom |
| U26, U27 | VTTX | (pluggable into Tyco 1888247-1 connector) | 2 | Bottom |
| U31 | SN74AUP1G08DBVR | 5-pin SOT-23 | 1 | Top or bottom |
| U30, U33 | TI TXB0104DR | SOIC14 | 2 | Top or bottom |
| U25 | Xilinx XCF32PFSG48C | FSG48 BGA | 1 | Top or bottom |
| U34 | SN74AUP1G00DBVR | 5-pin SOT-23 | 1 | Top or bottom |
| U35 | SN74LVC1G07DBVR | 5-pin SOT-23 | 1 | Top or bottom |
| U37 | MAX6709OUB | uMAX10 | 1 | Top |
| P1 | FCI71922-126LF | 26-pin connector | 1 | Bottom, thru-hole |
| P2, P3 | FCI75867-132LF | 8-pin connector | 2 | Bottom, thru-hole |
| P4 | Molex 87833-1420 | 14-pin connector | 1 | Bottom, thru-hole |
| P5, P6 | Samtec QSE-080-01-F-D | 160-pin connector | 2 | Bottom, surface mounted |
| P7 | Samtec HLE-108-02-F-DV-A | 8-pin connector | 1 | Bottom, surface mounted |
| SW1, SW3 | C&K TDA04H0SB1 | SM DIP switch | 2 | Top |
| SW2 | Omron B3U-1000P | SM push button | 1 | Top |
| D1..D11 | Lumex SML-LX1206GC-TR | SM LED | 11 | Top |
| L1..L10 | Delevan 5022-511J | SM inductor | 10 |  |
| R1..R147 | Resistors | SM0603 | 137 |  |
| C4, C7, C8, C10, C58, C74, C75, C73, C179, C190, C108, C165, C90, C91, C100, C147, C148, C156, C197, C198, C210, C226, C229 | Capacitor 47uF Kemet T520B476M006ATE025 | SM3528 | 23 |  |
| C36, C59, C11, C12, C37, C60 | Capacitor 100 uF T520B107M006ATE025 | SM3528 | 6 |  |
| C9 | Capacitor 330 uF Kemet T520D337M006ATE015 | SM7343 | 1 |  |
| C2, C5, C19, C20, C21, C22, C43, C44, C45, C27, C28, C50, C51, C65, C66, C33, C34, C56, C57, C71, C71, C186, C189, C219, | Capacitor 4.7uF AVX 06036D475KAT2A | SM0603 | 24 |  |
| All other capacitors |  | SM0603 |  |  |